## Slide 1: That QGIS 3 Metre Projection Message
A 60 year long story https://www.icsm.gov.au/datum/australian-geodetic-datum-196684-agd

## Slide 2: Today, in QGIS we see:

## Slide 3: A quick timeline
1954 – I was born – black and white TVs existed but arrived In Au 1956
1966 – ANS/AGD was developed – taught at UNSW, AMG 56, ISG 561, etc
1970s – the internet grew into a global thing – colour TVs in Au in 1975
1979 – I bought my first Personal Computer - Black &White – Music Tape
1983: GPS is made available for civilian use after Korean Air Lines Flight 007 is shot down
1984 – WGS84 was developed
1994 – GDA94 was developed – along with a 7 Parameter Transformation – a general 200m shift NE but no time stamp, MGA 56, MGA 561, etc
2020 GDA 2020 arrived, dealing with 2 difficult problems:
  10cm/year drifting – hence the time stamp
  30 years of much higher accuracy measurements
Delivering
  10,000,000 approximate 1.7m NTV2 vectors for ‘Accurate’ Transformations.
  A 7 Parameter Transformation that “best fits” the GDA 2020 Geoid to WGS84

## Slide 4: Really Early Theodilites
Before my time, 20 Seconds of Arc
+Old Survey Chain (22 Yards) with 100 Links (0.201168m ea)
State of the Art around 1970, 2 Seconds of Arc from memory

## Slide 5: Long Distance Measurement in the 50s
The Geodimeter (acronym of geodetic distance meter) was the first optical electronic distance meter surveying instrument.[1][2] It was originally developed for measuring the speed of light.[3][4] It was invented in 1947 by Erik Osten Bergstrand [sv] and commercialized in 1953 by the AGA (Aktiebolaget Gasaccumulator) company of Sweden
The original tellurometer, known as the Micro-Distancer MRA 1, was introduced in 1957.[1] It was invented by Trevor Wadley of the Telecommunications Research Laboratory of the South African Council for Scientific and Industrial Research (CSIR)

## Slide 6: Back in 1966
I was 12 years old, many here were not here, maybe some of your parents too…
Surveying equipment was limited
  Old Old Theodilies, 20 Seconds of Arc at best
  100 Yard Chains, in Links, Tellurometer and Geodimeter
  Accurate time pieces though
  No GPS though
The first official national Australian geodetic datum was actually called the Australian Geodetic Datum (AGD). It was proclaimed in the Australian Commonwealth Gazette No. 84 of 6 October 1966. The proclamation included the parameters of the local ellipsoid, known as the Australian National Spheroid (ANS), which defines the adopted size and shape of the earth, and the position of the origin point: Johnston Geodetic Station. The accompanying national map projection, a transverse Mercator projection that conforms to the internationally accepted Universal Transverse Mercator Grid system, was called the Australian Map Grid (AMG).

## Slide 7: Punch Cards to Desktop Computing
At UNSW (maybe 1975) we had to write a program in Fortran on ‘Punch Cards’
In 1978 I was writing a Least Squares Adjustment Program on Prof John Allman’s HP9810A (Reverse Polish Notation)

## Slide 8: Introducing GPS
The US Air Force launched the first prototype satellites of the Global Positioning System (GPS) in 1978. GPS used a larger constellation of satellites and improved signal transmission, thus improving accuracy. Early GPS observations required several hours of observations by a static receiver to reach survey accuracy requirements.
It really was an era of rapid technology advancement – including Surveying Equipment!!!
GPS Not only provides Longitude, Latitude and Height, but also very accurate date and times

## Slide 9: National Geodetic Adjustments
AGD coordinates were propagated throughout Australia from the 1966 national adjustment. There continued to be national re-adjustments of the AGD in subsequent years as new observations were introduced. Recognising the need for Australia to eventually move to a geocentric datum in October 1984, the National Mapping Council resolved to adopt the 1982 adjustment as a first step in that process. To distinguish between the two versions of the Australian Geodetic Datum, the different coordinate sets were referred to as AGD66/AMG 66 and AGD84/AMG84.
The final decision on adoption of the new adjustment was left to individual jurisdictions and only Queensland, South Australia and Western Australia adopted AGD84 with the other states and territories choosing to remain on AGD66.

## Slide 10: Introducing GDA94
The AGD provided a reference system that best fit the shape of the earth in the Australian Region but its origin did not coincide with the centre of mass of the earth. National datums were commonly non-geocentric before satellite based navigation systems were established in the early 1970’s
The distance between the origin points of GDA94 and AGD is approximately 200 metres. When the coordinates of a point on the Earth’s surface are converted from AGD to GDA94 this translates to a coordinate difference of approximately the same amount. The difference varies slightly depending on where you are in Australia.
NOTE: Australia’s Continental Drift is about 4 inches (10cm) per year, which is about the same rate as your finger nails grow. So 30 years would be 3m, not 200m, i.e. the 200m is a definition different in the 2 geoids.

## Slide 11: NSW with Continental Drift removed
Since GDA94, technical improvements, continental drift, and additional geodetic observations have all combined to mean that where we thought things were, we now think we know a better location.
The following image shows these (without the overwhelming continental drift) as:
NOTE: This is the root cause of the QGIS 3m warning

## Slide 12: There are 10,000,000 approximate 1.7m long shift NTV2 vectors
To do ACCURATE Transformations (back and forth) one MUST use Shift Vector interpolation (Too big to download, load to a Database, index, etc)
To do FAST but INACCURATE Transformations (back and forth) one uses a ‘Best Fit’ Seven Parameter Similarity Transformation

## Slide 13: TransXYZ.xls https://github.com/icsm-au/DatumSpreadsheets

## Slide 14: Source Code for ‘Best Fit’ 7 Parameter Similarity Transformation (Part 1)
Public Module GDA94_2020
Public Sub GDA92_GDA2020(lng94 As Double, lat94 As Double, hgt94 As Double, ByRef lng2020 As Double, ByRef lat2020 As Double, ByRef hgt2020 As Double)
Dim i7 As Double = (lat94 / 180) * Math.PI
Dim i8 As Double = (lng94 / 180) * Math.PI
Dim d9 As Double = hgt94
Dim d13 As Double = 6378137
Dim d14 As Double = 298.257222101
Dim d15 As Double = 1 / d14
Dim d16 As Double = 2 * d15 - d15 * d15
Dim d17 As Double = d13 / Math.Sqrt(1 - d16 * Math.Sin(i7) * Math.Sin(i7))
Dim l7 As Double = (d17 + d9) * Math.Cos(i7) * Math.Cos(i8)
Dim l8 As Double = (d17 + d9) * Math.Cos(i7) * Math.Sin(i8)
Dim l9 As Double = ((1 - d16) * d17 + d9) * Math.Sin(i7)
Debug.Print("L7: " + String.Format("{0:#########.000}", l7) + ", L8: " + String.Format("{0:#########.000}", l8) + ", L9: " + String.Format("{0:#########.000}", l9))
Dim g6 As Double = 61.55 / 1000
Dim g7 As Double = -10.87 / 1000
Dim g8 As Double = -40.19 / 1000
Dim g9 As Double = -9.994 / 1000
Dim g10 As Double = -39.4924 / 1000
Dim g11 As Double = -32.7221 / 1000
Dim g12 As Double = -32.8979 / 1000
Dim g14 As Double = ((g10 / 3600) / 180) * Math.PI
Dim g15 As Double = ((g11 / 3600) / 180) * Math.PI
Dim g16 As Double = ((g12 / 3600) / 180) * Math.PI
Dim g17 As Double = 1 + (g9 / 1000000)
Dim i19 As Double = Math.Cos(g15) * Math.Cos(g16)
Dim j19 As Double = Math.Cos(g15) * Math.Sin(g16)
Dim k19 As Double = -Math.Sin(g15)
Dim i20 As Double = Math.Sin(g14) * Math.Sin(g15) * Math.Cos(g16) - Math.Cos(g14) * Math.Sin(g16)
Dim j20 As Double = Math.Sin(g14) * Math.Sin(g15) * Math.Sin(g16) + Math.Cos(g14) * Math.Cos(g16)
Dim k20 As Double = Math.Sin(g14) * Math.Cos(g15)
Dim i21 As Double = Math.Cos(g14) * Math.Sin(g15) * Math.Cos(g16) + Math.Sin(g14) * Math.Sin(g16)
Dim j21 As Double = Math.Cos(g14) * Math.Sin(g15) * Math.Sin(g16) - Math.Sin(g14) * Math.Cos(g16)
Dim k21 As Double = Math.Cos(g14) * Math.Cos(g15)
Dim m19 As Double = l7
Dim m20 As Double = l8
Dim m21 As Double = l9
(Hacked from TransXYZ.xls into a dumb VB Subroutine – but importantly, it is only 2 pages of unoptimized source code)

## Slide 15: Source Code for ‘Best Fit’ 7 Parameter Similarity Transformation (Part 2)
Dim i23 As Double = (i19 * m19 + j19 * m20 + k19 * m21)
Dim i24 As Double = (i20 * m19 + j20 * m20 + k20 * m21)
Dim i25 As Double = (i21 * m19 + j21 * m20 + k21 * m21)
Dim g27 As Double = g17 * i23
Dim g28 As Double = g17 * i24
Dim g29 As Double = g17 * i25
Dim e31 As Double = g6 + g27
Dim e32 As Double = g7 + g28
Dim e33 As Double = g8 + g29
Debug.Print("E31: " + String.Format("{0:#########.000}", e31) + ", E32: " + String.Format("{0:#########.000}", e32) + ", E33: " + String.Format("{0:#########.000}", e33))
Dim d6 As Double = e31
Dim d7 As Double = e32
Dim d8 As Double = e33
Dim d20 As Double = Math.Sqrt(d6 * d6 + d7 * d7)
Dim d21 As Double = Math.Sqrt(d20 * d20 + d8 * d8)
Dim d22 As Double = Math.Atan((d8 / d20) * ((1 - d15) + (d16 * d13) / d21))
Dim d23 As Double = Math.Atan(d7 / d6)
If d23 < 0 Then d23 = d23 + Math.PI
Dim f23 As Double = d23 / Math.PI * 180
Dim d27 As Double = d8 * (1 - d15) + d16 * d13 * Math.Sin(d22) * Math.Sin(d22) * Math.Sin(d22)
Dim d28 As Double = (1 - d15) * (d20 - d16 * d13 * Math.Cos(d22) * Math.Cos(d22) * Math.Cos(d22))
Dim d24 As Double = Math.Atan(d27 / d28)
Dim f24 As Double = d24 / Math.PI * 180
Dim d25 As Double = d20 * Math.Cos(d24) + d8 * Math.Sin(d24) - d13 * Math.Sqrt(1 - d16 * Math.Sin(d24) * Math.Sin(d24))
lng2020 = f23
lat2020 = f24
hgt2020 = d25
Debug.Print("GDA2020 Decimal Long: " + String.Format("{0:#####.0000000}", lng2020) + ", Lat: " + String.Format("{0:#####.0000000}", lat2020) + ", Hght: " + String.Format("{0:#########.000}", hgt2020))
End Sub
End Module
Commercial Tools such as FME support both NTV2 and this transformation.

## Slide 16: Geoid to Mercator Projection
7 Parameter Similarity Transformations and NTV2 handle Geoid to Geoid transformations.
Redfearn, Robbins, Lambert formula handle Geoid  Projection transformations.
https://en.wikipedia.org/wiki/Transverse_Mercator_projection
It is all about using mathematics to make a slice of the world flat, and back again

## Slide 17: The QGIS Transformation Process
All we humans do is to nominate the
  Source Geoid/Projection "Coordinate Reference Number"
    and the
  Destination Geoid/Projection "Coordinate Reference Number“
the algorithm goes:
  Source E/N (Projected Coordinates)
    Reverse formula for Mercator, Lambert, etc
  Source Lat/Long (Geoid Coordinates)
    Reverse 7 Parameter Transformation
  WGS84 Lat/Long (Geoid Coordinates)
    Forward 7 Parameter Transformation
  Dest Lat/Long (Geoid Coordinates)
    Forward formula for Mercator, Lambert, etc
  Dest E/N (Projected Coordinates), skipping the first and last if not needed.

## Slide 18: Summing Up
Local Coordinate Systems
Australian Map Grid (AGD66/AMG 66) (1966) - Australian National Spheroid (ANS)
Australian Map Grid (AGD84/AMG84) (1984) – Qld, SA & WA Only
The World Geodetic System (WGS84) is used in Geodesy, GPS (etc).
Map Grid Australia (GDA94/MGA84) (1994) –
Map Grid Australia (GDA2020/MGA2020)
7 Parameter Similarity Transform is EXACT – both directions
7 Parameter Similarity Transform is EXACT – both directions
7 Parameter Similarity Transform is EXACT – both directions
7 Parameter Similarity Transform is EXACT – both directions
*** 7 Parameter Similarity Transform is an Approximation – both directions *** NTV2 Shift Vector Interpolation is EXACT – both directions – from/to all the above Geoids – with Robbin’s/Redfearn's transformations (Geoid<->Projection)